## Slide 1: Wastewater Treatment Facility Improvements Project Water Works Commission Wausau, WI June 25, 2019

## Slide 2: The Project Overview and Status Report

## Slide 3: Project will Address an Aging Facility
1939
1967
1988
80+ Years Old
50+ Years Old
30+ Years Old

## Slide 4: One of Wausau’s Most Valuable Assets
* Based on recent new 24-mgd nutrient-removing treatment facility for Denver, CO. Grand opening 2017. Cost = $417M.
[CCI 2018 = 10,959. CCI 2011 = 9070. Cost = $504M in $2018. Includes a 7-mile forcemain.]
Potential Value = $175M*

## Slide 5
Upgrade
Repurpose
New
Alternate

## Slide 6: Simple Site Rendering Showing New Structures
Chemical Storage
A/S Selector
Solids Processing
Administration/Lab
Flow Splitting
Secondary
(Alternate)

## Slide 7: Comprehensive Project to Address Passage of Time Since Last Major Upgrade
Equipment and Infrastructure
Water Quality Regulations (Phosphorus)
Safety Regulations (Fire and Explosions)
Biosolids Land Application Logistics and Cost Avoidance

## Slide 8: Schedule
2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Preliminary Layout Design
Detailed Design
Facility Plan
Bid
Construction
Submit CWF Application and
Plans/Specs to WDNR
Sep 30
Bids
Loan Closing
First Loan Draw
Begin Loan Re-Payment
Phased Rate Increase
Submitted Final Facility Plan to WDNR
Final Layout Drawings and Operating Strategies Complete. Design Advances to Specifications and Fine Details.

## Slide 9: After the Improvements are Operational

## Slide 10: Effluent Quality will Improve

## Slide 11: Historical Effluent BOD Data

## Slide 12
Chart: 2018 Effluent BOD Concentrations (mg/L)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Eau Claire BOD | 6.0161 | 5.6071 | 4.5032 | 4.9667 | 5.0645 | 4.2133 | 4.2935 | 4.7323 | 5.4433 | 4.7097 | 4.7621 | 8.0645
Wausau BOD | 18 | 13 | 10 | 7 | 14 | 15 | 20 | 14 | 18 | 14 | 25 | 26
Low WLA Limit | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
Chart: 2018 Flows (mgd)
| Average
Eau Claire Flow | 7.1983
Wausau Flow | 4.6175

## Slide 13
Chart: 2018 Effluent TSS Concentrations (mg/L)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Eau Claire TSS | 4.0645 | 3.25 | 2.4839 | 2.9667 | 2.4194 | 2.2333 | 2.6129 | 3 | 2.8333 | 3.1613 | 2.6897 | 3.871
Wausau TSS | 5 | 4 | 4 | 3 | 5 | 7 | 8 | 11 | 6 | 7 | 7 | 7

## Slide 14
Chart: 2018 Effluent TP Concentrations (mg/L)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Eau Claire TP | 0.2529 | 0.23357 | 0.23035 | 0.26643 | 0.22161 | 0.2347 | 0.28484 | 0.31632 | 0.21 | 0.20226 | 0.736 | 0.34184
Wausau TP | 0.684 | 0.627 | 0.771 | 0.595 | 0.793 | 0.969 | 0.886 | 1 | 0.77 | 0.671 | 0.796 | 0.728
Low TMDL | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981 | 0.34981
Current Limit | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Dec 31, 2025

## Slide 15
Eau Claire
Wausau
Mode A | Exceptional Effluent Quality and Stability
Mode B | Sufficient Effluent Quality, Poor Stability
Mode A is the preferred method to operate; however, it can cost more to operate than Mode B. It can be more energy intensive. The primary concern is alkalinity.

## Slide 17: Activated Sludge System: Minimize Operating Cost for Required Operating Mode
Operating Mode Flexibility ► Match Mode (Cost) to Required Performance
Efficient Aeration System ► Minimize Aeration Energy
  Equipment, Configuration, and Automation
Nitrate Utilization ► Minimize Aeration Energy, Supplemental Alkalinity
  Reduce Aeration Requirement
  Enhance Alkalinity Recovery
Enhance Biological Phosphorus Removal ► Reduce Chemicals
  Balance with Biosolids Operating Cost
Chemical Feed Automation► Reduce Chemicals
$
Performance
Flexibility and Provisions to Maximize Efficiency

## Slide 18: Biosolids Logistics will Improve

## Slide 19: Biosolids Logistics will Improve
Produce Dry Class A EQ Material that is Unregulated
Investigating Potential Outlets
  Hsu Growing Supply – Produce a Product Bagged or Bulk [e.g., WauSoil]
    Initial Conversation Encouraging: Interested
    Donohue Provided Information and Samples
    Next Steps: Provide Samples, Tour a Drying Facility
  Marathon County Landfill – Meeting in Early July | Free Daily Cover
  Local Fertilizer Dealers/Co-Ops – Future Conversations
  Large Local Cash Croppers [High Confidence] – Future Conversations
Rothschild Biomass Plant
  WDNR Permit Precludes Municipal Solid Waste and Biosolids

## Slide 20: Equipment and Automation Strategies will Enhance Efficiency

## Slide 21: Equipment will be More Efficient
Electrical Equipment – Focus on Energy Funding
  LED Lights, Premium Efficiency Motors, VFDs, Automation
Gas-Consuming Equipment – Focus on Energy Funding
  High Efficiency Dual-Fuel and Natural Gas Boilers
Process Automation
  Electricity
  Chemicals
  Labor
Efficient HVAC Strategies
  Recover Some Blower Heat | Fresh Air for Tunnel and Digester Complex

## Slide 22: Ventilation Rates will Increase

## Slide 23: Ventilation Rates will Increase
Preliminary Treatment 12 ac/hr
Gas Handling 12 ac/hr
Biosolids Building 6 ac/hr [dewatering, screening, and pumping]
Digester Complex 6 ac/hr
Tunnel 6 ac/hr
NFPA 820
Standard for Fire Protection in Wastewater treatment and Collection Facilities

## Slide 24: Near-Term Maintenance Spending will Decrease

## Slide 25: Initial Annual Cost Accounting

## Slide 26: Developing a Sustainable Design

## Slide 27: Deliberately Focus on Cost-Effective Sustainability Practices
Meeting Mid-to-Late July
  Discuss and Adopt Sustainability Concepts

## Slide 28: Thank You